## Slide 1: Getting Started with MODFLOW 6
Introduction to Groundwater Modeling using MODFLOW

## Slide 2: Outline
Workflow
What’s in the distribution
Simulation
  Temporal discretization
  Numerical Solution
  Groundwater Flow (GWF) Model

## Slide 3: What is MODFLOW?
A computer program for hydrologic simulation (traditionally groundwater flow)
Command line executable program
Runs on Windows, Mac, and Linux
Written in Fortran (mf6 is object oriented)
Reads text and binary input files
Writes text and binary output files

## Slide 4: MODFLOW Simulation Workflow
MODFLOW Program
Input Files
Output Files
Graphical User Interface
(GUI)
or
FloPy

## Slide 5: MODFLOW Simulation Workflow
MODFLOW Program
Input Files
Output Files
Much of the focus of this class will be on this part of the workflow

## Slide 6: MODFLOW 6 Distribution
Zip file available from USGS website
Unzipped

## Slide 7: Github Releases
https://github.com/MODFLOW-USGS/modflow6/releases

## Slide 8: Distribution Content

## Slide 9: Distribution Content
bin
  mf6 (exe and dll)
  mf5to6 (converter mf2005 to mf6)
  zbud6 (ZONEBUDGET program)
doc
  Release notes
  Input and output guide
  Supplemental technical information
  Example description
  Reports
examples
  Lots and lots of examples…

## Slide 10: Important User Information

## Slide 11: MODFLOW 6 Publications
Hughes, J.D., Langevin, C.D., and Banta, E.R., 2017, Documentation for the MODFLOW 6 framework: U.S. Geological Survey Techniques and Methods, book 6, chap. A57, 40 p., https://doi.org/10.3133/tm6A57.
Langevin, C.D., Hughes, J.D., Banta, E.R., Niswonger, R.G., Panday, Sorab, and Provost, A.M., 2017, Documentation for the MODFLOW 6 Groundwater Flow Model: U.S. Geological Survey Techniques and Methods, book 6, chap. A55, 197 p., https://doi.org/10.3133/tm6A55.
Provost, A.M., Langevin, C.D., and Hughes, J.D., 2017, Documentation for the "XT3D" option in the Node Property Flow (NPF) Package of MODFLOW 6: U.S. Geological Survey Techniques and Methods, book 6, chap. A56, 40 p., https://doi.org/10.3133/tm6A56.

## Slide 12: MODFLOW 6 Publications (cont)
Langevin, C.D., Provost, A.M., Panday, Sorab, and Hughes, J.D., 2022, Documentation for the MODFLOW 6 Groundwater Transport Model: U.S. Geological Survey Techniques and Methods, book 6, chap. A61, 56 p., https://doi.org/10.3133/tm6A61.
Hughes, J.D., Leake, S.A., Galloway, D.L., and White, J.T., 2022, Documentation for the Skeletal Storage, Compaction, and Subsidence (CSUB) Package of MODFLOW 6: U.S. Geological Survey Techniques and Methods, book 6, chap. A62, 57 p., https://doi.org/10.3133/tm6A62.

## Slide 13: Examples
55 example problems
Described in mf6examples.pdf
Described in online document
All examples available as FloPy scripts

## Slide 14: Simulation

## Slide 15: Simulation Types
Single Model
Multiple Models

## Slide 16: Simulation Components
Timing Module
Solutions
Models
Exchanges
Utilities

## Slide 17: LGR Simulation
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2

## Slide 18: GWF Exchanges
Simulation
Iterative Model Solution
PARENT
Temporal Discretization
C1
GC
C2
PARENT-C1
PARENT-C2
C1-GC

## Slide 19: Multi-Model Coupling
Any number of models can be included in a simulation
Models coupled at matrix level
Flexibility supports coupling of parent, child, grandchild models, stacked models or adjacent models

## Slide 20: Multi-Model Concept

## Slide 21: Blocks and Keywords
MODFLOW-2005 DIS
MODFLOW 6 DIS

## Slide 22: Blocks and Keywords
Notes: Human readable
Better error trapping
Easily allows new options to be added, without breaking backward compatibility
Most blocks support OPEN/CLOSE

## Slide 23: Simulation Name File
Required even for common case with one model
Named mfsim.nam
One simulation per folder
# Simulation name file
BEGIN OPTIONS
END OPTIONS
BEGIN TIMING
TDIS6 ps1.tdis
END TIMING
BEGIN MODELS
GWF6 ps1.nam ps1
END MODELS
BEGIN EXCHANGES
END EXCHANGES
BEGIN SOLUTIONGROUP 1
IMS6 ps1.ims ps1
END SOLUTIONGROUP

## Slide 24: Temporal Discretization
Simulation uses the concepts of “stress periods” and “time steps”
For each stress period user specifies
  PERLEN—Length of the stress period
  NSTP—Number of time steps in the stress period
  TSMULT—time step multiplier
For most problems, TSMULT is 1., so that each time step in PERLEN / NSTP

## Slide 25: Choosing Stress Periods
Pumping
Recharge
Time
Stress Periods and Time Steps
Time
For large stress changes, may be necessary to use short time steps right after the change (use TSMULT > 1 for this)

## Slide 26: Choosing Stress Periods
Pumping
Recharge
Time
Stress Periods
Time

## Slide 27: Temporal Discretization
BEGIN OPTIONS
TIME_UNITS days
END OPTIONS
BEGIN DIMENSIONS
NPER 1
END DIMENSIONS
BEGIN PERIODDATA
1.0 1 1.0
END PERIODDATA

## Slide 28: Time and Length Units
Length and Time Units must be consistent for all data
  For example ft and days:
    Flow – cubic feet per day (ft3/d)
    Hydraulic conductivity – feet per day (ft/d)
    Transmissivity – square feet per day (ft2/d)
    Recharge flux – feet per day (ft/d)
    Time step length – days
    Specific storage – per ft (1/ft)
MODFLOW lets you specify the units, but MODFLOW does not convert input data based on the units being used– the units specification is just for user information

## Slide 29: Solutions
Used to solve one or more models
The only solution available now is the Iterative Model Solution, or IMS
IMS solves the following nonlinear equation
  Ax = b

## Slide 30: IMS Input File
BEGIN OPTIONS
COMPLEXITY SIMPLE
END OPTIONS
BEGIN NONLINEAR
END NONLINEAR
BEGIN LINEAR
END LINEAR

## Slide 31: Groundwater flow (gwf) model

## Slide 32: Groundwater Flow (GWF) Model
First model available in MODFLOW 6
Synthesizes capabilities in
  MODFLOW-2005
  MODFLOW-NWT
  MODFLOW-USG
  MODFLOW-LGR
  MODFLOW-CDSS

## Slide 33: Groundwater Flow Equation

## Slide 34: Control-Volume Finite-Difference

## Slide 35: Finite-Difference Equation

## Slide 36: Generalized CVFD Equation

## Slide 37: Rearranged for Solution

## Slide 38: Iteration

## Slide 39: Fundamental GWF Packages
The GWF Model in MODFLOW 6 uses the concept of a “package” to manage and activate capabilities
Packages are specified in the GWF name file
Package Name | Abbreviation
Discretization | DIS
Initial Conditions | IC
Node-Property Flow | NPF
Storage | STO
Constant Head | CHD
Well | WEL
Drain | DRN
River | RIV
General-Head Boundary | GHB
Recharge | RCH
Evapotranspiration | EVT

## Slide 40
Storage (STO)
Node Property Flow (NPF)
Horizontal Flow Barrier (HFB)
Specified Head (CHD)
Observations (OBS)
Recharge (RCH)
Output Control (OC)
Discretization (DIS, DISV, DISU)
Initial Conditions (IC)
Well (WEL)
Groundwater Flow (GWF) Model
Data Input
Internal Flow
Hydrologic Stress
Internal Flow
Stream-Flow Routing (SFR)
Multi-Aquifer Well (MAW)
Lake (LAK)
Advanced Stress Package
Unsaturated Zone Flow (UZF)
Water Mover
(MVR)
Compaction and Subsidence (CSUB)
Ghost Node Correction (GNC)
River (RIV)
General-Head Boundary (GHB)
Evapo-transpiration (EVT)
Drain (DRN)
Buoyancy (BUY)
Viscosity (VSC)

## Slide 41: Example GWF Name File
BEGIN OPTIONS
END OPTIONS
BEGIN PACKAGES
DIS6 ps1.dis
IC6 ps1.ic
NPF6 ps1.npf
OC6 ps2.oc
CHD6 ps1.chd
END PACKAGES

## Slide 42: All GWF Packages

## Slide 43: Spatial Discretization
Three ways to enter grid
  DIS – regular MODFLOW grid
  DISV – discretization by vertices
  DISU – fully unstructured

## Slide 44: Discretization (DIS) Package
“Regular MODFLOW grid”
Consists of layers, rows, and columns
Top and bottoms can have variable elevations

## Slide 45: DIS Input File

## Slide 46: DIS Input File

## Slide 47: DIS Input File

## Slide 48: DIS Input File
Binary Grid File

## Slide 49: Which representation is correct?

## Slide 50: Caution with Vertical Offsets
MODFLOW does not connect cells on adjacent sides of the red line.

## Slide 51: Example DIS Input File
BEGIN OPTIONS
LENGTH_UNITS FEET
END OPTIONS
BEGIN DIMENSIONS
NLAY 3
NROW 21
NCOL 20
END DIMENSIONS
BEGIN GRIDDATA
DELR
CONSTANT 500.
DELC
CONSTANT 500.
TOP
CONSTANT 350.
BOTM LAYERED
CONSTANT 220.
CONSTANT 200.
CONSTANT 0.
END GRIDDATA

## Slide 52: Initial Conditions
Specify starting heads
A head value below cell bottom elevation will start the cell as dry
Always required, even for steady-state simulations

## Slide 53: Node Property Flow (NPF) Package
Calculates conductance between cells
Manages cell wetting and drying
Can invoke an optional XT3D formulation

## Slide 54: Conductance Equations

## Slide 55: Prisms in Series

## Slide 56: Horizontal Conductance

## Slide 57: NPF Input File

## Slide 58: NPF Input File
ICELLTYPE=0: cell is treated as confined for conductance calculations
ICELLTYPE=1: cell converts between confined and unconfined depending on head

## Slide 59: NPF Input File
K
K22
K33

## Slide 60: NPF Input File
Conductivity ellipsoid (for any cell) can be rotated around its three axes

## Slide 61: NPF Input File
XT3D Option more robust, but computationally expensive

## Slide 62: NPF Input File
MODFLOW rewetting can be used to reactivate cells that have gone dry
Rewetting is no longer recommended. Use Newton-Raphson instead!

## Slide 63: NPF Input File
Vertical conductance calculation: DEFAULT (most stable)

## Slide 64: NPF Input File
Vertical conductance calculation: VARIABLECV

## Slide 65: NPF Input File
Vertical conductance calculation: VARIABLECV and DEWATERED

## Slide 66: NPF Input File
Vertical flow calculation: PERCHED

## Slide 67: Constant Head (CHD) Package
Fixes the head in a cell at the user-prescribed value. This value change from one time step to the next.
Should be used with caution because there is no limit to the volume of water that can be lost to or provided from constant head cells.

## Slide 68: CHD Input File

## Slide 69: CHD Input File
MAXBOUND is the maximum number of constant head cells that will be active in any stress period.

## Slide 70: CHD Input File
List of constant head cells. These cells will remain as constant head cells until another PERIOD block is encountered.

## Slide 71: CHD Input File
Auxiliary variables

## Slide 72: CHD Input File

## Slide 73: CHD Input File
PRINT_INPUT: echo input to the listing file
PRINT_FLOWS: write calculated CHD flows to the listing file
SAVE_FLOWS: write calculated CHD flows to budget file

## Slide 74: CHD Input File
Variables shown in blue can be represented using time series. Values are interpolated each time step from a user-provided time series record.

## Slide 75: Example CHD Input File
BEGIN OPTIONS
PRINT_INPUT
PRINT_FLOWS
SAVE_FLOWS
END OPTIONS
BEGIN DIMENSIONS
MAXBOUND 42
END DIMENSIONS
BEGIN PERIOD 1
# canal
1 1 1 330.0
1 2 1 330.0
1 3 1 330.0
1 4 1 330.0
...
# river
1 1 20 320.0
1 2 20 320.0
1 3 20 320.0
...
END PERIOD